## Slide 1: Embedded 3D Scanner with ESP32-S3 and the Sharp GP2Y0A51SK0F Infrared Sensor
Final course project · Embedded System Design (ESDS437064E)
Lecturer: M.Sc. Huỳnh Hoàng Hà
No. | Full name | Student ID
1 | Huỳnh Anh Tuấn | 24119096
2 | Lê Thành Tài | 24119080
3 | Phan Anh Khoa | 24119048
GitHub: https://github.com/YaePak/DESIGN-AND-IMPLEMENTATION-OF-AN-ESP32-S3-BASED-3D-SCANNING-SYSTEM
Notes: Introduce the team and the project: a low-cost turntable 3D scanner controlled by an ESP32-S3, using an infrared triangulation sensor.

## Slide 2: Goal: digitise small objects with one low-cost sensor
≈120 mm
max object diameter
150 mm
max height, 1 mm layers
100
points per turn (3.6°)
±1–2 mm
target on a 60 mm cube
Requirements
Starts at power-on, no buttons
Streams each layer over Wi-Fi
Data kept in RAM only
Closed STL model on the PC
Why it is embedded
Real-time stepper timing
Analog sampling on ADC2
Two FreeRTOS tasks, two cores
Framed TCP with ACK/NACK

## Slide 3: TF-Luna cannot see the object; the Sharp sensor can
Criterion | TF-Luna | Sharp (final)
Principle | time of flight | triangulation
Range | 0.2–8 m | 2–15 cm
Accuracy | ±6 cm | ≈0.2–1 mm
Interface | UART / I²C | 1 analog pin
Calibration | not needed | voltage table
At 30–90 mm | no | yes
Decision
Object is 30–90 mm away
That is inside the TF-Luna 20 cm blind zone
Sharp is built for 2–15 cm

## Slide 4: Triangulation: distance moves the light spot on the PSD
Nearer object → spot moves further on the PSD → higher Vo
Vo is turned into millimetres with a calibration table

## Slide 5: The reading depends on the surface (1/2)
Notes: Matte white paper gives the cleanest spot; that is why the test cube was wrapped in A4 paper.

## Slide 6: The reading depends on the surface (2/2)
Notes: Translucent tape pulled faces in by 11–15 mm. Grazing angles and edges are filtered on the ESP32 and on the PC.

## Slide 7: System overview

## Slide 8: Pin allocation and control board
Pin | Function
4 / 5 / 6 | table DIR/STEP/EN
10 / 11 / 12 | Z DIR/STEP/EN
18 | Sharp Vo (ADC2)
17 | unused input
5V · 3V3 | 5 V regulator, logic
No push button: the scan starts at power-on, RST starts a new scan
Control board schematic

## Slide 9: Firmware: two tasks that only meet in RAM

## Slide 10: Measuring one point next to Wi-Fi
The problem
ADC2 shares the radio with Wi-Fi
While Wi-Fi sends, a read can return ≈0 mV
The PCB cannot be changed
irMeasure()
Wait 30 ms to settle
Read 24 samples, 1 ms apart
Drop ≈0 mV reads
Mean of the middle 50 %
CAL table → d, r = 90 − d

## Slide 11: From 24 raw samples to one radius
Example point: Vo = 940 mV → d = 60 mm → r = 30 mm

## Slide 12: Motion timed to cancel table vibration
22 ms
between the 2 steps of a move
25 steps
per 1 mm layer
0–150 mm
Z range, returns home

## Slide 13: A transfer the PC can verify
Why it is safe
PC counts the lines
A late PC still gets the whole scan
Lost link: resend from RAM

## Slide 14: PC side: correcting the 14.1 mm beam offset
Red: raw points, green: true 60 mm square
xyztostl.py: offset fix, grazing filter, gap fill, binary STL

## Slide 15: Hardware built
Printed frame
Board, component side
Board, copper side
4×4 test cube
Cube in A4 paper
Sensor on the Z axis

## Slide 16: 60 test runs, no functional error
22
firmware runs
18
receiver runs
28
mesh builder runs
36 %
ADC errors still OK
Unmodified firmware against a simulated machine and real TCP sockets
Covered: no object, late PC, Wi-Fi loss, NACK, tall object, bad input
Simulated 60 mm cube → 60.7–60.9 mm, 0.35 mm RMS
22 + 18 + 28 = 68 program runs: 8 tests run firmware and receiver together

## Slide 17: Results on the 60 mm cube: ±1–2 mm met
Case | Result | Remark
Sim, no correction | 71.6 × 71.1 mm | pinwheel
Sim, e = 14.1 mm | 60.8 × 60.9 mm | 0.35 mm RMS
Real, tape, old table | 65.8 × 66.7 mm | translucent
Real, A4 paper | 62.3 × 62.5 mm | side 61.3 mm (+1.3)

## Slide 18: Real scan: stable from bottom to top
100/100
points per layer
0.0 %
ADC errors
7.9 s
per 1 mm layer
Notes: Points drop at z ≈ 55 mm: the beam is 10 mm above the table, so the top is at 65 mm, the real cube height.

## Slide 19: Limitations and future work
Limitations
Surface-dependent sensor
No Z home switch
No top surface
No colour
CAL set on the test cube
Embedded
Z limit switch
ADC1 or ADS1115
STEP pulses from RMT / timer
AI and features
AI auto-calibration
Top-surface scan
Colour output
Point-cloud completion

## Slide 20: A working low-cost scanner, built around the sensor's real behaviour
Automatic scan · robust ADC next to Wi-Fi · verified transfer · closed STL
Demo video: https://www.youtube.com/watch?v=GfAV5bEJ8As
Thank you for listening
Notes: Fill in the GitHub link before submitting.